## Slide 1: Chapter 6 Functions of Combinational Logic

## Slide 2: Half, Full Adder & Parallel Adder

## Slide 3: Simple Addition

## Slide 4: Binary Addition

## Slide 7: Adder Introduction
An adder is a digital logic circuit in electronics that implements addition of numbers. In many computers and other types of processors, adders are used to calculate addresses, similar operations and table indices in the ALU and also in other parts of the processors. These can be built for many numerical representations like excess-3 or binary coded decimal.

## Slide 8: Adders Are Classified Into Two Types
Half Adder and Full Adder.
The half adder circuit has two inputs: A and B.
It add two input digits and generate a carry and sum.
The full adder circuit has three inputs: A, B and C.
It add the three input numbers and generate a carry and sum

## Slide 9: Half Adder
Using Half Adder, you can design simple addition with the help of logic gates.
Let’s see an addition of single bits.
0+0 = 0
0+1 = 1
1+0 = 1
1+1 = 10

## Slide 10: Half Adder
These are the least possible single-bit combinations. But the result for 1+1 is 10, the sum result must be re-written as a 2-bit output. Thus, the equations can be written as 0+0 = 00
0+1 = 01
1+0 = 01
1+1 = 10
The output ‘1’of ‘10’ is carry-out. ‘SUM’ is the normal output and ‘CARRY’ is the carry-out.

## Slide 11: Half Adder

## Slide 12: Half Adder Truth Table

## Slide 13: Half Adder Expression

## Slide 14: What is Half Adder Circuit
The half adder adds two binary digits called as augend and addend.
Half adder produces two outputs as sum and carry.
XOR is applied to both inputs to produce sum.
AND gate is applied to both inputs to produce carry.

## Slide 15: Full Adder
The difference between a half-adder and a full-adder is that the full-adder has three inputs and two outputs.
Whereas half adder has only two inputs and two outputs.
The first two inputs are A and B and the third input is an input carry as CIN.
When a full-adder logic is designed, you string eight of them together to create a byte-wide adder and cascade the carry bit from one adder to the next.

## Slide 16: Full Adder

## Slide 17: Full Adder Truth Table

## Slide 18: Full Adder Truth Table
The full adder logic can be implemented with the truth table.
The output S is an XOR between the input A and the half-adder, SUM output with B and C-IN inputs.
Take C-OUT will only be true if any of the two inputs out of the three are HIGH.

## Slide 19: Full Adder Logic Circuit

## Slide 20: What Is Full Adder Circuit
The full adder adds 3 one bit numbers.
Where two can be referred to as operands.
One can be referred to as bit carried in.
It produces 2-bit output, and these can be referred to as output carry and sum.

## Slide 21: Full Adder Logic Circuit
We can implement a full adder circuit with the help of two half adder circuits.
First, half adder will be used to add A and B to produce a partial Sum.
A second half adder logic can be used to add C-IN to the Sum produced by the first half adder to get the final S output.
If any of the half adder logic produces a carry, there will be an output carry.

## Slide 22: Full Adder Logic Circuit
We can implement a full adder circuit with the help of two half adder circuits.
First, half adder will be used to add A and B to produce a partial Sum.
A second half adder logic can be used to add C-IN to the Sum produced by the first half adder to get the final S output.
If any of the half adder logic produces a carry, there will be an output carry.

## Slide 23: Full Adder Logic Circuit
A C-OUT will be an OR function of the half-adder Carry outputs.
The implementation of larger logic diagrams is possible with full adder logic.

## Slide 24: Making Full Adder Using Half Adder

## Slide 25: Parallel Adder

## Slide 27: Four-Bit Parallel Adders

## Slide 28: Adder Expansion: Constructing 8 bit Adder using 4 bit Adder IC

## Slide 31: Adder Application (Voting Machine)

## Slide 33: 2 Bit Multiplier

## Slide 34: Design 3 Bit & 4 Bit Multiplier

## Slide 35: Comparator

## Slide 36: MAGNITUDE COMPARATOR: DIGITAL COMPARATOR
It is a combinational logic circuit.
Digital Comparator is used to compare the value of two binary digits.
There are two types of digital comparator
(i) Identity Comparator
(ii) Magnitude Comparator.

## Slide 37
IDENTITY COMPARATOR: This comparator has only one output terminal for when A=B, either A=B=1 (High) or A=B=0 (Low)
MAGNITUDE COMPARATOR: This Comparator has three output terminals namely A>B, A=B, A<B. Depending on the result of comparison, one of the output will be High (1).
Block Diagram of Magnitude Comparator is shown in Fig. 1

## Slide 38: BLOCK DIAGRAM OF MAGNITUDE COMPARATOR

## Slide 39: 1- Bit Magnitude Comparator
This magnitude comparator has two inputs A and B and three outputs AB.
This magnitude comparator compares the two numbers of single bits.
Truth Table of 1-Bit Comparator

## Slide 41: K-Maps For All Three Outputs

## Slide 50: 3-bit Comparator
To design 3-bit comparator.
Number of inputs 6 A2,A1,A0, B2,B1,B0
Total number of combination 2^6=64
Huge truth table then K-map so traditional method is complex.
We need another approach to design a comparator circuit.

## Slide 51
Designing general equation for comparator.
In this example we are comparing 3 bits two inputs.
A2 & B2 are MSB. A0 & B0 are LSB.
It compares each of these bits in one number with bits in that of other number and produces one of the following outputs as A = B, A < B and A>B. The output logic statements of this converter are

## Slide 52
If A2 = 1 and B2 = 0, then A is greater than B (A>B). Or
If A1 and B2 are equal, and if A1 = 1 and B1 = 0, then A > B. Or
If A2 and B2 are equal & A1 and B1 are equal, and if A0 = 1, and B0 = 0, then A>B. Or

## Slide 53: Equation
A>B = A2B2’ + (A2 Ex-Nor B2)A1B1’ + (A2 Ex-Nor B2)(A1 Ex-Nor B1)A0B0’
A<B = A2’B2 + (A2 Ex-Nor B2)A1’B1 + (A2 Ex-Nor B2)(A1 Ex-Nor B1)A0’B0
A=B =(A2 Ex-NOR B2) (A1 Ex-NOR B1) (A0 Ex-NOR B0)

## Slide 54: 4-Bit Comparator IC

## Slide 55: 8-Bit Comparator

## Slide 57: Cascading of Comparator

## Slide 58: MUX & DMUX

## Slide 59: Multiplexer (MUX)
Many to One

## Slide 60: Multiplexer (data Selectors)
Definition : A multiplexers (MUX) is a device that allows digital information from several sources to be routed onto a single line for transmission over that line to a common destination.
Several data input lines
Some select line (less than the no. of input lines)
Single output line
If there are n data input lines and m select lines, then

## Slide 61: Functional Diagram Of a Multiplexer

## Slide 62: 2 : 1 Multiplexer

## Slide 63: 4 : 1 Multiplexer

## Slide 64: 4:1 MUX Timing Diagram

## Slide 65: Logic Gates Implementation Using MUX

## Slide 66: Implementation Of Logic Functions using Multiplexer

## Slide 68: 4:1 MUX using 2:1 MUX

## Slide 69: Multiplexer Tree

## Slide 70: Cascading of MUX

## Slide 71: Demultiplexer (Data Distributor)
Definition : A DEMULTIPLEXER (DEMUX) basically reverses the multiplexing function. It takes data from one line and distributes them to a given number of output lines. For this reason, the demultiplexers is also known as a data distributor.
Single data input line.
Some select line (less than the no. of output lines)
Several output line
If there are n data output lines and m select lines, then

## Slide 72: Functional Diagram Of a Demultiplexer

## Slide 73: 1 : 2 Demultiplexer

## Slide 74: 1 : 4 Demultiplexer

## Slide 75: 1:4 DMUX Timing Diagram

## Slide 76: DECODERS

## Slide 77: Definition
An important part of the system which selects the cells to be read from and written into is the decoder.
– Accepts a value and decodes it
• Output corresponds to value of n inputs
• It also is called many-to-one decoder, a decoder matrix or simply a decoder.

## Slide 79: A decoder consists of

## Slide 82: What a decoder does

## Slide 83: How can you build a 2-to-4 decoder?

## Slide 84: A picture of a 2-to-4 decoder

## Slide 85: Enable inputs

## Slide 90: BCD (Binary Coded Decimal)
Binary coded decimal (BCD) is a system of writing numerals that assigns a four-digit binary code to each digit 0 through 9 in a decimal (base-10) numeral.
The four-bit BCD code for any particular single base-10 digit is its representation in binary notation.
4bit can make 16 combination but in BCD we only uses start 10 combinations.

## Slide 95: BCD-Decimal Decoder Waveform

## Slide 97: Common Anode (CA)

## Slide 98: Common Cathode (CC)

## Slide 105: ENCODERS

## Slide 106: Encoders

## Slide 113: Code Converters